## Slide 1: “DMR–based optimization of LNG Liquefaction via MCHE Parameters & MR Composition Variation in ASPEN PLUS Simulation Software”
Under the guidance of
Dr. Shraddha Rani Singh,
HOD (Chemical Dept.)
Team Members
Sanjit Pal
Maryam Banoo
Sanyam Dixit
Radhakrishna Pathak
Tooba Parsa

## Slide 2: Table Of Contents
Introduction
Problem Statement
Project Objectives
Important Literature Review
Methodology
Characteristics Of Optimal Design
Expected Outcomes
Industrial Relevance
References
Questionnaire

## Slide 3: Introduction
As we know, Energy demand is observably increasing due to many factors, including population growth and the improvement of living standards. Global energy consumption is estimated to increase by about 1 /3 by 2040, with fossil fuels being the main energy source.
According to Shell’s 2021’ liquefied natural gas (LNG) outlook report, the global demand for LNG will reach 700 million tons by 2040. at the same time, the number of LNG-fueled shipments is also increasing.
The liquefaction unit is the main unit in the LNG plant that functions to cool down natural gas from a gaseous to a liquefied state. However, this unit consumes a lot of energy compared to other units.

## Slide 4: …contd.
LNG liquefies from a gaseous state by reducing its temperature to -160 degrees C.
The main advantage of the liquefaction process is due to its economical feasibility in which LNG will only take 1/600th of volume compared to natural gas in gaseous form.
One of the equipment is the Main Cryogenic Heat Exchanger (MCHE). This equipment plays an important role in the overall performance of the liquefaction unit, yet there are only a few studies done especially in terms of the internal performance of MCHE. Therefore, simulation is the best way to analyze the phenomena that take inside the MCHE.

## Slide 5: Problem Statement
To model and simulate, using Aspen Plus, the performance of the MCHE process and then study the post-effects of these changes in downstream equipment, connected in the DMR refrigeration cycle.

## Slide 6: Project Objectives
Model Development: Develop a comprehensive Aspen Plus simulation model of an LNG liquefaction unit, including all relevant process units and equipment, with a particular emphasis on the Main Cryogenic Heat Exchangers (MCHE).
Parameter Variation: Investigate the impact of varying key parameters associated with the MCHE, such as temperature, pressure, flow rates, and heat exchange areas, on the overall efficiency and performance of the LNG liquefaction process.
Efficiency Analysis: Assess the thermal efficiency, heat transfer efficiency, and energy consumption of the MCHE under different parameter scenarios.

## Slide 7: Project Objectives
Optimization: Use the simulation model to identify optimal operating conditions for the MCHE that result in improved energy efficiency, reduced operational costs, and enhanced LNG production.
Sensitivity Analysis: Perform sensitivity analyses to understand how changes in MCHE parameters affect the entire liquefaction process and its components.
Validation & Recommendation: Validate the simulation results against real-world data or published literature to ensure the accuracy and reliability of the Aspen Plus model, then provide recommendations for optimizing MCHE parameters in practical LNG liquefaction operations.

## Slide 8: Important Literature Review
Ait-Ali’s (1979) optimization study on mixed refrigerant process operation proved to be a major contribution to the refrigeration processes. Importance was placed on decreasing the compressor’s power and numerous simplifications were considered to attain that target.
Gao, Lin, and Gu (2009) performed an optimization study on an LNG process for coal bed methane (CBM) within the simulation package HYSYS.
Lee et al. (2002) The optimization was performed using a consecutive method. The system’s key parameters were optimized in sequential order: composition of components, discharge pressures, and temperatures of the heat exchanger.
Kanoglu et al. (2001) highlighted the advantages of replacing the Joule Thomson valve (JT) instead of the turbine
expander for LNG expansion units.
Renaudin et al. (1995) tested the impact of exchanging mixed refrigerant expansion and LNG valves using liquid turbines.

## Slide 9: …contd.
Gandhi Raju (2009) specified the ‘acclaimed’ composition of mixed refrigerants for precooled systems claiming the ‘optimal’ composition of refrigerant. Gandhi Raju (2009) proposed that using and executing the technology in operational plants is challenging, as the necessary compositions differ intensely with varying plant conditions and schemes.
Paradowski et al. (2004) performed parametric research on a pre-cooled propane mixed refrigerant cycle. Their study investigated mixed refrigerant composition, propane cycle pressures, precooling temperature, and propane cycle compressor speed.
Saffari (2009) optimized the energy efficiency of an industrial pre-cooled propane mixed refrigerant LNG base load plant by varying the components of refrigerants and the mole fractions in liquefaction and sub-cooling cycles.
Castillo et al. (2012) in their paper “Conceptual analysis of the precooling stage for LNG processes” made a comparison between different precooling cycles for LNG processes which were carried out through computational simulation using Aspen HYSYS.

## Slide 10: Plan of Work
Our research will follow a structured methodology which is as follows:
  Literature Review
  Data collection
  Modelling
  Defining Properties
  Parameter Variation
  Sensitivity Analysis of Efficiency Data
  Optimization Cycle
  Conclusion
  Recommendation(s)
  Paper Writing
  Submission of Paper to a reputable journal in the field of Chemical Engg

## Slide 11: Methodology
Acquiring knowledge and information about MCHE: Information such as the geometrical properties of MCHE, correlations for heat transfer calculation, and phase equilibrium will be identified. Other than that, the method for simulating the MCHE will be determined.
Simulating and verifying the proposed MCHE by using Aspen Plus Simulation Software: Once all the criteria for developing the simulation are confirmed, the activity for developing the simulation can be validated using Aspen Plus. The simulation’s results will be verified against the experimental result.
Collecting and analyzing data from the field: The operating data from the field will be collected and it will be analyzed in terms of its reliability and suitability for the study.
Scaling up the simulation and implementing the data: The simulation built earlier will be scaled up to the actual process. Once it is ready, the collected data will be implemented in the completed simulation.

## Slide 12: Methodology
Verifying and analyzing the result: The simulation’s result will be verified against the expected result obtained from the study or the actual process condition. Then, it will be analyzed especially for the relationship between refrigerant composition and heat integration performance.
Implementing and evaluating the proposed solution for improving the MCHE: Based on the analysis, a suitable solution will be proposed for improving the MCHE. It will be then implemented in the simulation to investigate its impact on the overall liquefaction process. The feasibility of the proposed solution will be evaluated technically and economically.
Simulating the proposed solution of MCHE for examining the different compositions of MR: Based on the efficient parameters combination for MCHE parameters, a suitable combination of Mixed Refrigerants will be proposed for improving the process efficiency for minimizing energy consumption.

## Slide 13: Characteristics of optimal design
Characteristic | Variable(s)
High Heat Transfer Coefficient Low Pressure drop Small Space or area | Stream Temperatures Flow rates of Streams Fouling Factor Fluid Properties (Density, Specific Heat, Viscosity, Thermal Conductivity, etc.) Varying the use of different correlations for calculating heat transfer coefficient in Aspen Plus
4. Low Temperature Crossover | Minimum temperature approach > zero
5. Gas should liquify completely (no vapor fraction) | 
Simulation can be done for various operating conditions such as: Variation in feed composition Variation in ambient temperature Variation in flow rates. | 

## Slide 14: Expected Outcomes
A detailed Aspen Plus simulation model of an LNG liquefaction unit.
Insights into the optimal operating conditions for MCHE in LNG
liquefaction.
Recommendations for process optimization and energy efficiency improvements.
Practical implications for the LNG industry in terms of reducing
operational costs and environmental impact.

## Slide 15: Industrial Relevance
Optimizing the LNG liquefaction process by thoroughly
examining
Varying the parameters associated with the MCHE using
Aspen Plus simulation.
Other studies and projects related to LNG production and process optimization, several factors set this project apart, such as-Top of Form:

## Slide 16: …contd.
Detailed MCHE Parameter Variation
Suitable MR composition
Aspen Plus Simulation.
Holistic Approach: We assess how changes in MCHE parameters & and MR composition affect the overall efficiency, energy consumption, and cost-effectiveness of the entire process.
Industry Relevance: By optimizing MCHE parameters, we contribute to cost savings, reduced environmental impact, and improved competitiveness in the LNG sector.
Practical Recommendations: Our project not only identifies optimal
operating conditions but also provides practical recommendations for process improvement.

## Slide 17: References
1) A. Aspelund, T. Gundersen, J. Myklebust, M.P. Nowak, A.
Tomas Gard (2009) An optimization-simulation model for a
simple LNG process, Elsevier, Computers and Chemical
Engineering 34 (2010) 1606-1617
2)
Technology for Small-Scale LNG IOP Conf. Ser.: Earth
Environ. Sci. 459 052094
3) M. M. Faruque Hasan (2010) Modelling and optimization of
& Biomolecular Engineering, National University of
Singapore
4) Matias Vikse et al. (2018), Simulation of Dual Mixed
Refrigerant Natural Gas Liquefaction Process Using a Non-
smooth Framework, MDPI, Processes 6, 193 (2018), 1-16
5) Lee GC, Smith R, Zhu XX. (2002) Optimal synthesis of
mixed-refrigerant systems for low-temperature processes.
41:5016–5028
6) Kyungjae Tak, Wonsub Lima, Kwangho Choib, Daeho Kob, Il
Moo, (2011), Optimization of mixed-refrigerant system in
LNG liquefaction process, Elsevier B.V. 1st European
Symposium on Computer Aided Process Engineering –
ESCAPE 21, E.N. Pistikopoulos, M.C. Georgiadis and A.C.
kokossis (Editors) 1824-1828.
L G Lunkova et al (2020) The Natural Gas Liquefaction 7) Barclay, M., & Denton, N. (2005). Selecting offshore LNG
processes. LNG Journal, 10(1),
8) Flynn, T. M. (2005). Cryogenic engineering (2nd ed. revised
and expanded). New York: Marcel Dekker
a Liquefied Natural Gas Process, Thesis, Dept of Chemical 9) Del Nogal FL, Kim J, Perry SJ, Smith R. Integrated approach
for the design of refrigeration and power systems.
Presented in the 6th Topical Conference on Natural Gas
Utilization, AIChE Annual Spring National Meeting, Florida,
USA, 2006
10) Del Nogal F, Kim JK, Perry S, Smith R. Optimal design of
mixed refrigeration cycles. Industrial & Engineering
Chemistry Research. 2008; 47:8724–8740.
Industrial and Engineering Chemistry Research. 2002; 11) Demetri EP. A general method for the analysis of compact
multi-fluid heat exchangers. Presented in the American
Society of Mechanical Engineers, Paper 72–HT.14, 1973

## Slide 18
Thank You !!
Now, you can ask your query